# Specimen engineering designs for cooling towers and condensers

## Where to sample in an installation - general guide

(Refer also to guidance from L8 Legionnaires' Disease Health and Safety Executive paper [1]. Other member states might have their own versions of such guides.)

## Cooling systems including cooling towers and evaporative condensers

#### Typical cooling tower

Red = return to cooling tower

Sampling cooling systems

- Ideally sample from somewhere on the return to cooling tower

- Neutralise biocides where possible, for more detail see [2]

Outbreak investigation samples from cooling systems should be taken:

- From the warmest point

- Possibly from the pond (furthest away from fresh water inlet ball valve if possible)

- Supply water / Make up water

- Foam (slime) from pack, and other components

- Biofilm

- Any others suggested by the risk assessment

- HSE (2008) Control of Legionella bacteria in water systems ISBN 978 0 7176 1772 2

- ENVIRONMENT AGENCY (2005) The determination of Legionella bacteria in waters and other environmental samples http