Examples of environmental sites for sampling for Legionellae provided by [1]

| Site | Approximate number of samples | Volume of samples |
| --- | --- | --- |
| General potable water system |
| Incoming water pipe(s) | 2 | 10 litres |
| Water softener (pre and post) | 2 | 1 litre |
| Preheater (discharge side) | 1 | 1 litre |
| Primary heater (discharge side) | 1 | 1 litre |
| Circulating pumps | 2 | 1 litre |
| Holding tanks (cold water, discharge side) | 2 | 1 litre |
| Expansion tank for hot water | 1 | 1 litre |
| Back drain on sprinkler system(s) | 2 | 1 litre |
| Fireline where it branches off main system | 1 | 1 litre |
| Water used for respiratory therapy equipment | 2 | ≥1 litre |
| Outlets in patients' rooms | 4 | 1 litre |
| Air compressor system |  |  |
| Vacuum water source | 1 | ≥100 ml |
| Positive pressure equipment side |  |  |
| Condensate from tank(s) | 3 | ≥100 ml |
| Water separator(s) directly off compressors | 4 | ≥100 ml |
| Water source(s) near air intake(s) | 4 | ≥100 ml |
| Air samples where patients were ill with legionellosis | 3 | n.a. |
| Potable water final distribution outlets |  |  |
| Haemodialysis water source |  |  |
| Before or after demineralizer | 1 | ≥100 ml |
| Intensive care units |  |  |
| Respiratory therapy (patients' room) | 2 | 1 litre |
| Cardiac | 2 | 1 litre |
| Services with different geographical locations | 7 | 1 litre |
| Ice-maker (entry water) and ice ( |  | ≥1 litre |
| Air-conditioning system |
| Air handling unit serving area where disease occurred | 2 | ≥100 ml |
| Cooling towers |  |  |
| Return from heat exchanger to water (spray/trough and gutter) distribution or pond (sump) | 2 | (≥1 litre |
| Water supply | 1 | 1 litre |
| Hot tubs |  |  |
| Pool and balance tank (if fitted) | 1 | 1 litre |
| Jets and pipes | 1 | swab |
| Other |
| Decorative fountain | 1 | 1 litre |
| Creeks, ponds, sites of stagnant water | 4 | 1 litre |

n.a. = not applicable

Source: Adapted from Barbaree et al., 1987

- BARTRAM J. (2007) Legionella and the prevention of legionellosis WHO, Geneva ISBN 92 4 156297 http pdf